參數位址皆為16進位格式

| Address | Parameter | Meaning | R/W | Range | Default |
| --- | --- | --- | --- | --- | --- |
|  | //LED Flag |  |  |  |  |
| 0x0000 | LED Flag | TX、RX、AL1、AL2 LED亮滅旗標 | read only | 0000~1111 | 0 |
|  | //PV of Ch01~Ch05 |  |  |  |  |
| 0x0001 | Channel 1 PV | 通道1顯示值 | read only (RSP Write) | -1999~9999 | 0 |
| 0x0002 | Channel 2 PV | 通道2顯示值 | read only (RSP Write) | -1999~9999 | 0 |
| 0x0003 | Channel 3 PV | 通道3顯示值 | read only (RSP Write) | -1999~9999 | 0 |
| 0x0004 | Channel 4 PV | 通道4顯示值 | read only (RSP Write) | -1999~9999 | 0 |
| 0x0005 | Channel 5 PV | 通道5顯示值 | read only (RSP Write) | -1999~9999 | 0 |
|  | //PVOF of Ch01~Ch05 |  |  |  |  |
| 0x0006 | Channel 1 PV offset | 通道 1顯示值的設定偏差值 | R/W | -1000~1000 | 0 |
| 0x0007 | Channel 2 PV offset | 通道 2顯示值的設定偏差值 | R/W | -1000~1000 | 0 |
| 0x0008 | Channel 3 PV offset | 通道 3顯示值的設定偏差值 | R/W | -1000~1000 | 0 |
| 0x0009 | Channel 4 PV offset | 通道 4顯示值的設定偏差值 | R/W | -1000~1000 | 0 |
| 0x000A | Channel 5 PV offset | 通道 5顯示值的設定偏差值 | R/W | -1000~1000 | 0 |
|  | //Alarm 1 Set point |  |  |  |  |
| 0x000B | Alarm 1 Set point Ch 01 | 警報1對應通道1的設定值 | R/W | -1000~1000 | 0 |
| 0x000C | Alarm 1 Set point Ch 02 | 警報1對應通道2的設定值 | R/W | -1000~1000 | 0 |
| 0x000D | Alarm 1 Set point Ch 03 | 警報1對應通道3的設定值 | R/W | -1000~1000 | 0 |
| 0x000E | Alarm 1 Set point Ch 04 | 警報1對應通道4的設定值 | R/W | -1000~1000 | 0 |
| 0x000F | Alarm 1 Set point Ch 05 | 警報1對應通道5的設定值 | R/W | -1000~1000 | 0 |
|  | //Alarm 2 Set point |  |  |  |  |
| 0x0010 | Alarm 2 Set point Ch 01 | 警報2對應通道1的設定值 | R/W | -1000~1000 | 0 |
| 0x0011 | Alarm 2 Set point Ch 02 | 警報2對應通道2的設定值 | R/W | -1000~1000 | 0 |
| 0x0012 | Alarm 2 Set point Ch 03 | 警報2對應通道3的設定值 | R/W | -1000~1000 | 0 |
| 0x0013 | Alarm 2 Set point Ch 04 | 警報2對應通道4的設定值 | R/W | -1000~1000 | 0 |
| 0x0014 | Alarm 2 Set point Ch 05 | 警報2對應通道5的設定值 | R/W | -1000~1000 | 0 |
|  | //Alarm 1 Function Setting |  |  |  |  |
| 0x0015 | Alarm 1 Function | 警報1功能設定 | R/W | FU index | None |
| 0x0016 | Alarm 1 Mode | 警報1模式設定 | R/W | MD index | None |
| 0x0017 | Alarm 1 Hysteresis | 警報1遲滯值設定 | R/W | -1000~1000 | 0 |
|  | //Alarm 2 Function Setting |  |  |  |  |
| 0x0018 | Alarm 2 Function | 警報2功能設定 | R/W | FU index | None |
| 0x0019 | Alarm 2 Mode | 警報2模式設定 | R/W | MD index | None |
| 0x001A | Alarm 2 Hysteresis | 警報2遲滯值設定 | R/W | -1000~1000 | 0 |
|  | //Alarm timer unit |  |  |  |  |
| 0x001B | Alarm timer unit | 警報延遲時間單位 (目前保留無使用) | X | X | X |
|  | //Channels |  |  |  |  |
| 0x001C | Channels Number | 通道數量 | R/W | 1~5 | 5 |
| 0x001D | Channels Scan Time | 通道依序播放時間 | R/W | 0~10 | 0 |
|  | //Communication |  |  |  |  |
| 0x001E | ID address | Modbus通訊ID address設定 | R/W | 1~255 | 1 |
| 0x001F | BAUD RATE | Modbus通訊鮑率設定 | R/W | BAUD index | 9600 |
| 0x0020 | RTU | Modbus通訊RTU設定 | R/W | RTU index | N81 |
|  | //Key level LOCK |  |  |  |  |
| 0x0021 | Level lock | 表頭按鍵階層鎖定 | R/W | LOCK index | 0001 |
|  | //Type of Ch01~Ch05 |  |  |  |  |
| 0x0022 | Input type of Ch 01 | 通道1的輸入類型 | R/W | TYPE index | TC_K |
| 0x0023 | Input type of Ch 02 | 通道2的輸入類型 | R/W | TYPE index | TC_K |
| 0x0024 | Input type of Ch 03 | 通道3的輸入類型 | R/W | TYPE index | TC_K |
| 0x0025 | Input type of Ch 04 | 通道4的輸入類型 | R/W | TYPE index | TC_K |
| 0x0026 | Input type of Ch 05 | 通道5的輸入類型 | R/W | TYPE index | TC_K |
|  | //Unit of Ch01 ~ Ch05 |  |  |  |  |
| 0x0027 | Input unit of Ch 01 | 通道1的單位顯示 | R/W | UNIT index | °C |
| 0x0028 | Input unit of Ch 02 | 通道2的單位顯示 | R/W | UNIT index | °C |
| 0x0029 | Input unit of Ch 03 | 通道3的單位顯示 | R/W | UNIT index | °C |
| 0x002A | Input unit of Ch 04 | 通道4的單位顯示 | R/W | UNIT index | °C |
| 0x002B | Input unit of Ch 05 | 通道5的單位顯示 | R/W | UNIT index | °C |
|  | //DP of Ch01~Ch05 |  |  |  |  |
| 0x002C | Dot point of Ch 01 | 通道1的小數點位置 | R/W | DP index | 0000 |
| 0x002D | Dot point of Ch 02 | 通道2的小數點位置 | R/W | DP index | 0000 |
| 0x002E | Dot point of Ch 03 | 通道3的小數點位置 | R/W | DP index | 0000 |
| 0x002F | Dot point of Ch 04 | 通道4的小數點位置 | R/W | DP index | 0000 |
| 0x0030 | Dot point of Ch 05 | 通道5的小數點位置 | R/W | DP index | 0000 |
|  | //Linear Low & High of Ch01 |  |  |  |  |
| 0x0031 | Linear Low of Ch 01 | 通道1線性輸入低點對應值 | R/W | -1999~9999 | 0 |
| 0x0032 | Linear High of Ch 01 | 通道1線性輸入高點對應值 | R/W | -1999~9999 | 1000 |
|  | //Linear Low & High of Ch02 |  |  |  |  |
| 0x0033 | Linear Low of Ch 02 | 通道2線性輸入低點對應值 | R/W | -1999~9999 | 0 |
| 0x0034 | Linear High of Ch 02 | 通道2線性輸入高點對應值 | R/W | -1999~9999 | 1000 |
|  | //Linear Low & High of Ch03 |  |  |  |  |
| 0x0035 | Linear Low of Ch 03 | 通道3線性輸入低點對應值 | R/W | -1999~9999 | 0 |
| 0x0036 | Linear High of Ch 03 | 通道3線性輸入高點對應值 | R/W | -1999~9999 | 1000 |
|  | //Linear Low & High of Ch04 |  |  |  |  |
| 0x0037 | Linear Low of Ch 04 | 通道4線性輸入低點對應值 | R/W | -1999~9999 | 0 |
| 0x0038 | Linear High of Ch 04 | 通道4線性輸入高點對應值 | R/W | -1999~9999 | 1000 |
|  | //Linear Low & High of Ch05 |  |  |  |  |
| 0x0039 | Linear Low of Ch 05 | 通道5線性輸入低點對應值 | R/W | -1999~9999 | 0 |
| 0x003A | Linear High of Ch 05 | 通道5線性輸入高點對應值 | R/W | -1999~9999 | 1000 |
|  | //Linear CUT of Ch01~Ch05 |  |  |  |  |
| 0x003B | Linear CUT Ch 01 | 通道1線性輸入限制對應值 | R/W | CUT index | None |
| 0x003C | Linear CUT Ch 02 | 通道2線性輸入限制對應值 | R/W | CUT index | None |
| 0x003D | Linear CUT Ch 03 | 通道3線性輸入限制對應值 | R/W | CUT index | None |
| 0x003E | Linear CUT Ch 04 | 通道4線性輸入限制對應值 | R/W | CUT index | None |
| 0x003F | Linear CUT Ch 05 | 通道5線性輸入限制對應值 | R/W | CUT index | None |
|  | //The right side LED 8 Setting |  |  |  |  |
| 0x0040 | The right side LED 8 Setting | 錶頭右側下方最後一個 LED亮滅與否 | R/W | 0 : OFF 1 : ON | 0 |
|  | //old PV of Ch01~Ch05 |  |  |  |  |
| 0x1000 | old Channel 1 PV | 通道1顯示值 | read only | -1999~9999 | 0 |
| 0x1001 | old Channel 2 PV | 通道2顯示值 | read only | -1999~9999 | 0 |
| 0x1002 | old Channel 3 PV | 通道3顯示值 | read only | -1999~9999 | 0 |
| 0x1003 | old Channel 4 PV | 通道4顯示值 | read only | -1999~9999 | 0 |
| 0x1004 | old Channel 5 PV | 通道5顯示值 | read only | -1999~9999 | 0 |
|  | //LED Flag |  |  |  |  |
| 0x1005 | old LED Flag | TX、RX、AL1、AL2 LED亮滅旗標 | read only | 0000~1111 | 0 |
| 0x1006 | LED Alarm SP Flag | AL1、AL2各通道 LED亮滅旗標 | read only | 0000~1111 | 0 |

| Condition | Parameter | Option | Code | Meaning | Note1 |
| --- | --- | --- | --- | --- | --- |
|  | Alarm Function | None | 00 | 無警報 |  |
|  |  | Hi | 01 | PV高於AxSP觸發警報 |  |
|  |  | Lo | 02 | PV低於 AxSP觸發警報 |  |
|  | Alarm mode | None | 00 | None |  |
|  |  | Stdy | 01 | stand by |  |
|  |  | LAtH | 02 | latch |  |
|  |  | StLA | 03 | stand by+latch |  |
|  | BAUD RATE | 9600 | 00 | 9600 |  |
|  |  | 19200 | 01 | 19200 |  |
|  |  | 38400 | 02 | 38400 |  |
|  |  | 57600 | 03 | 57600 |  |
|  |  | 115200 | 04 | 115200 |  |
|  | RTU | N81 | 00 | N81 |  |
|  |  | N82 | 01 | N82 |  |
|  |  | O81 | 02 | O81 |  |
|  |  | E81 | 03 | E81 |  |
|  | LOCK | 0001 | 01 | 所有參數可看但不可調整 |  |
|  |  | 0010 | 02 | 第一階層可調整 |  |
|  |  | 0011 | 03 | 第一、二階層可調整 |  |
|  |  | 0100 | 04 | 第一、二、三階層可調整 |  |
|  | TYPE | TC_J | 00 | TC J type |  |
|  |  | TC_K | 01 | TC K type |  |
|  |  | TC_T | 02 | TC T type |  |
|  |  | TC_R | 03 | TC R type |  |
|  |  | D-PT | 04 | D-PT |  |
|  |  | LINE | 05 | LINE |  |
|  |  | RSP | 06 | RSP |  |
|  | UNIT | No_disp | 00 | No_disp | LINE、RSP可選擇 |
|  |  | °C | 01 | °C | 皆可選擇 |
|  |  | °F | 02 | °F | 皆可選擇 |
|  |  | % | 03 | % | LINE、RSP可選擇 |
|  |  | RH | 04 | RH | LINE、RSP可選擇 |
|  |  | % RH | 05 | % RH | LINE、RSP可選擇 |
|  |  | PPM | 06 | PPM | LINE、RSP可選擇 |
|  |  | blank 1 | 07 | blank 1 | LINE、RSP可選擇 |
|  | DP | 0000 | 00 | 無小數點顯示 |  |
|  |  | 000_0 | 01 | 顯示至小數點後一位 |  |
|  |  | 00_00 | 02 | 顯示至小數點後二位 |  |
|  |  | 0_000 | 03 | 顯示至小數點後三位 |  |
|  | CUT | None | 00 | No CUT |  |
|  |  | Lo | 01 | CUT on linear Low |  |
|  |  | Hi | 02 | CUT on linear High |  |
|  |  | Hi_Lo | 03 | CUT on linear High & Low |  |